## Slide 2
Chapter 18
Footings, Foundations, and Concrete

## Slide 3: Objectives
Describe the procedure for staking out a house location.
List the major considerations when designing a footing for a residential foundation.
Analyze a residential building project to determine the appropriate type of foundation wall.

## Slide 4: Objectives
Discuss the design considerations for wood, concrete, and masonry foundation walls.
Calculate the load to be supported by a beam.
Describe the characteristics of concrete, concrete blocks, masonry, and pavers used in residential construction.

## Slide 5: Staking Out House Location
Site plan provides necessary dimensions
Measuring tape, contractor’s level, and possibly a transit are required
Locate each corner of house
Use 9-12-15 unit method for square corners
Check accuracy by diagonal measurement

## Slide 6: 9-12-15 Unit Method
Goodheart-Willcox Publisher

## Slide 7: Batter Boards in Place
Goodheart-Willcox Publisher

## Slide 8: Excavation
Top soil should be removed and saved
Backhoe is generally used to excavate
Excavation for footings should extend at least 6" into undisturbed earth and at least 6" below frost penetration
No backfilling under footings

## Slide 9: Excavation
Must be large enough to allow space to work on the foundation
Excavation wall should slope away from bottom of the excavation
  Gentle slope in sandy soil
  Nearly vertical in clay

## Slide 10: Footings
Increase supporting capacity of foundation wall
  Size is typically based on foundation wall thickness
Footings are generally poured concrete
Goodheart-Willcox Publisher

## Slide 11: Footing Specifications
Thickness generally equals foundation wall thickness; width is twice the wall thickness
  Poor soil may require wider footings
Footings should be large enough to minimize differences in settlement
Check code recommendations
Use steel reinforcement bars (rebar)

## Slide 12: Fireplace and Chimney Footings
More massive than regular house footings
  Should be reinforced with steel
  12 inches thick
  Extend 6 inches beyond perimeter of chimney
  Cast integrally with house footing

## Slide 13: Stepped Footing
Steps should be multiples of 8 inches in masonry construction
Goodheart-Willcox Publisher

## Slide 14: Foundation Walls
Extend from first floor to footing
May also be basement walls
Variety of materials may be used
  Cast concrete, concrete block, pressure-treated wood, and stone or brick

## Slide 15: Types of Foundation Walls
Goodheart-Willcox Publisher

## Slide 16: T-Foundation Application
Goodheart-Willcox Publisher

## Slide 17: Slab Foundations
Slab foundation
  Extension of slab floor (monolithic slab foundation)
  Cast when the floor is placed
  Should extend below frost line
  Reinforcement is recommended
  Advantages: Less time, labor, and expense

## Slide 18: Stem Wall
Stem wall
  Typically used in crawl space foundation or slab foundation
  May be part of monolithic slab foundation or may be poured separately
  Often used in hurricane-prone areas

## Slide 19: Slab Foundation Application
Goodheart-Willcox Publisher

## Slide 20: Pier and Column Foundations
  Difference between piers and columns is height
Pier foundation
  Sometimes replaces T-foundation under house
  Often used in long crawl space
Post (column) foundation
  Used in basements where span is too long
  Column has a footing and post

## Slide 21: Parts of a Pier Foundation
Goodheart-Willcox Publisher

## Slide 22: Post (Column) Foundation
Goodheart-Willcox Publisher

## Slide 23: Wood Foundations
Wood foundations
  Below-grade, pressure-treated, plywood-sheathed stud wall
  Popular where winter weather stops construction
  Accepted by IRC
  Used in basement or crawl space construction

## Slide 24: Wood Foundations
Determine feasibility of using wood as opposed to concrete in areas with high water tables or high rainfall
Check local building codes
Check chemicals used to preserve wood
Green Architecture

## Slide 25: Wood Foundation Construction
Excavation should allow for 2" sand or 6" crushed stone for the footing
Base must be perfectly level
Footing plates are 2 × 8, 2 × 10, or 2 × 12 pressure-treated material
Foundation walls are 2 × 4 or 2 × 6 stud frame

## Slide 26: Wood Foundation Construction
Fasteners are silicon bronze, copper, or zinc-coated steel
Sheathing is pressure-treated plywood
All framing lumber is pressure-treated
Screed board nailed inside of foundation wall
Backfill after basement floor has cured and first floor is installed

## Slide 27: Concrete and Masonry Basement Walls
Factors influencing strength and stability:
  Height and thickness of wall
  Bond of mortar in masonry wall
  Vertical loading
  Support from crosswalls, pilasters, wall stiffeners
  Support from first floor framing
Lateral earth pressure can vary

## Slide 28: Pilasters
May be used to strengthen basement walls
Built at the same time as wall
Masonry wall pilasters are usually 8" × 16" in an 8" thick wall
Distance between pilasters should not exceed 15' in an 8" wall and 18' in a 10" wall
Also used to stiffen foundation walls

## Slide 29: Pilasters
Goodheart-Willcox Publisher

## Slide 30: Wall Stiffeners
Alternative to pilasters
#4 bar is placed in one core of block from footing to top plate
Another method is horizontal steel joint reinforcement at 16" intervals vertically

## Slide 31: Basement Wall Construction
Top of wall should be at least 8" above the grade in frame construction
Anchor wood sills to basement wall
Provide at least 7' 5" headroom
Anchor load-bearing crosswalls w/ metal tie bars

## Slide 32: Basement Wall Construction
Solid cap used to spread load over wall
Damp-proofing required on outside of basement wall
  Parge coat and sealer
Excess groundwater removal system may be needed

## Slide 33: Basement Wall Section
Goodheart-Willcox Publisher

## Slide 34: Beams and Girders
Support floor joists over long spans
May be wood or metal
  Wood beams may be built up or solid
  Steel beams may be S-beams or W-beams
Bearing wall supports part of load

## Slide 35: Structure Loads
Size of beam is based on weight of structure
Live load
  Fixed or moving weights (furniture, appliances, occupants, snow on roof)
Dead load
  Weight of structure itself (roofing, siding, joists)

## Slide 36: Weight Supported by Beam
Shaded area represents weight supported by W-beam
Goodheart-Willcox Publisher

## Slide 37: Load Assumptions
First floor and second floor
  Live load + dead load = 50 pounds per square foot
Ceiling
  Live + dead load = 30 pounds per square foot
Walls
  Dead load = 10 pounds per square foot
Roof
  No load on beam

## Slide 38: Weight Calculations: Example
Two-story frame structure
  28' × 40'
Area of house
  1120 sq. ft. per floor
Wall area
  320 sq. ft. per wall
Assumes bearing wall on each floor
Goodheart-Willcox Publisher

## Slide 39: Weight Calculations: Example
Weight of first floor = 56,000 lbs
Weight of second floor = 56,000 lbs
Weight of ceiling = 33,600 lbs
Total weight = 145,600 lbs
Half bears on the beam = 72,800 lbs
First + second floor wall weight = 6,400 lbs
Weight bearing on the beam = 79,200 lbs

## Slide 40: Beam Calculations: Example
Length of beam = 40 feet
Three columns reduce span to 10'-0" and 19.8 kips
  1 kip = 1000 lbs
8" × 6 1/2" WF beam will support 23 kips

## Slide 41: Beam Calculations: Example
Three supporting posts are added
Goodheart-Willcox Publisher

## Slide 42: Post Calculations: Example
Post selection
  Size is determined by weight to be supported and length of post
  Post must support 26 kips
  Post length is 8 feet
  3" post will support 34 kips

## Slide 43: Lintels
Lintel
  Horizontal structural member that supports load over opening
Made of precast concrete, cast-in-place concrete, lintel blocks, or steel angles
Bearing surface of steel angle lintel extends into the masonry at least 4"

## Slide 44: Types of Lintels
Goodheart-Willcox Publisher

## Slide 45: Concrete
Ordered by cubic yard
“Six-bag mix” recommended
Composed of cement, sand, large aggregate, and water
Work air pockets out by vibrating or tamping

## Slide 46: Concrete Finishing
Screed is used to smooth the surface
Float is used to embed large aggregate, remove imperfections, and consolidate mortar
Trowel is used to develop a hard, smooth surface

## Slide 47: Contraction Joints
Contraction joints are used to minimize and control cracking
Place in line with interior columns
Place at changes in width of slab
Maximum spacing of joints is 20 feet

## Slide 48: Floor Slabs
Concrete floor slab should be placed on 4" to 6" of compacted sand
Slab thickness is 4" minimum
Slabs should not be bonded to footings or columns
1" thick sand cushion may be used to separate slab from footing

## Slide 49: Concrete Blocks
Hollow concrete masonry units form exterior and interior walls
  Nominal size: 8 × 8 × 16
  Actual size:
  7-5/8" × 7-5/8" × 15-5/8" allows for 3/8" mortar joint
Goodheart-Willcox Publisher

## Slide 50: Paving
Rigid paving system
  Compacted subgrade, base, reinforced concrete slab, mortar setting bed, pavers w/ mortars joints
Flexible paving system
  Installed on compacted sand, crushed stone
  Rigid edge restraint prevents creep

## Slide 51: Aptitudes and Abilities
Aptitude
  Natural talent
  Ability to learn something quickly and easily
Ability
  Skill developed with practice
Employability