## Slide 2
Chapter 19
Sill and Floor Construction

## Slide 3: Objectives
Describe the components of a floor system.
Explain the difference between platform and balloon framing.
Determine proper joist sizes using a typical span data chart.
Plan the appropriate floor support using joists or trusses for a structure.

## Slide 4: Objectives
Select the appropriate engineered wood products for specific applications in residential construction.
Explain the principles of post and beam construction.

## Slide 5: Introduction
Framing methods vary from one section of the country to another
Two basic types of floor framing are platform framing and balloon framing
  Use plates, joists, and studs
Post and beam construction is used for walls and floors

## Slide 6: Platform Framing
Floor joists form platform on which walls rest
  Another platform rests on top of walls when there is a second story
Advantages include:
  Easy and fast to construct
  Shrinkage is uniform
  Platform provides a firestop between floors

## Slide 7: Platform Framing
The sill is starting point in constructing a floor
  Lowest member of structure’s frame
  Rests on foundation
  Supports floor joists or studs
  Generally 2 x 6 lumber
  Box sill construction generally used in platform framing

## Slide 8: Platform Framing
Box sill construction
Goodheart-Willcox Publisher

## Slide 9: Platform Framing
Box sill construction
Detail of first and second floor
Goodheart-Willcox Publisher

## Slide 10: Balloon Framing
Wall studs rest directly on the sill plate
Each floor “hangs” from the studs
Advantages: Small potential shrinkage, good vertical stability
Disadvantages: Less safe work surface, need to add firestops
Two types of sill construction: Solid (standard) or T-sill

## Slide 11: Solid (Standard) Sill Construction
Studs nailed directly to sill and joists
No header used
Goodheart-Willcox Publisher

## Slide 12: T-sill Construction
Header rests on sill
Serves as firestop
Studs rest on sill
Nailed to header and to sill plate
Goodheart-Willcox Publisher

## Slide 13: Balloon Framing
First and second floor construction
Joists supported by a ribbon and nailed to studs on second floor level
Goodheart-Willcox Publisher

## Slide 14: Joists and Beams
Joists provide support for floor
Usually made from southern yellow pine, fir, larch, hemlock, or spruce
Engineered wood and metal joists also available
Floor joists range in size from 2 x 6 to 2 x 12

## Slide 15: Using a Span Data Table
Select species of wood to be used
Select appropriate live load
Determine lumber grade to be used
Scan the lumber grade row and note maximum spans
Select joist size and spacing that will support desired live load and dead load

## Slide 16: Span Data: Example
Span is 14'-0; Number 1 dense southern pine
Live load is 30 pounds per square foot
Chart shows following choices:
  2 x 8 joists 12"OC or 16"OC
  2 x 10 joists 12"OC, 16"OC, or 24"OC
  2 x 12 joists 12"OC, 16"OC, or 24"OC
Best selection: 2 x 8 joists, 16"OC, will span up to 14'-5"

## Slide 17: Steel Floor Joists
Depths typically 6" to 12"
Thicknesses from 0.033" to 0.097"
Common spacing 24"OC, but other spacing also used

## Slide 18: Engineered Floor Joists
Sustainable alternative to solid wood joists
Can be made from wood chips and other wood products formerly considered waste
Stronger, and can span longer distances than solid wood joists
Fewer joists needed to meet building codes
Green Architecture

## Slide 19: Joists
Size based on span, load, species and grade of wood, and joist spacing
  When using metal joists, consider gauge of metal instead of species and grade of lumber
Spaced 12", 16", or 24"OC

## Slide 20: Beams
When span too great for unsupported joists, beam or load-bearing wall reduces span
Beam can be solid timber, built-up, or metal S- or W-beam
Load-bearing walls may be concrete block, cast concrete, or frame construction

## Slide 21: Supporting Floor Joists with Beams
Goodheart-Willcox Publisher

## Slide 22: Supporting Partition Walls
Partition walls that run parallel to floor joists require added support
Goodheart-Willcox Publisher

## Slide 23: Openings in Floor
Openings in the floor for stairs and chimneys required double joist framing
Goodheart-Willcox Publisher

## Slide 24: Cross Bridging
Stiffens floor, spreads load over broader area
Bridging boards or metal bridging are used
Goodheart-Willcox Publisher

## Slide 25: Floor Trusses
Rigid frameworks support loads over spans
Used in place of floor joists in residential construction
Consist of top chord, bottom chord, and web
  Chords are horizontal flanges on top and bottom of truss
  Web is truss framework between the chords

## Slide 26: Engineered Floor Trusses
Designed using computers
Usually fabricated from 2 x 4 or 2 x 6 lumber and spaced 24"OC
Have built-in cambers
Stress-graded lumber reduces material used
Webs may be metal or wood

## Slide 27: Subfloor
Affixed to top of floor joists
Provides surface for underlayment
Made from plywood, tongue-and-groove boards, common boards, and other panel products

## Slide 28: Installing Subfloor Panels
Joist spacing must be accurate
All panel edges must be supported
Goodheart-Willcox Publisher

## Slide 29: Cantilevered (Overhanging) Joists
Section of floor projects beyond a lower level
When floor joists run perpendicular to cantilevered section, longer joists form cantilever
When joists are parallel to overhanging area, cantilevered joists are required

## Slide 30: Cantilevered Joists
Joists should extend inside the structure twice the distance they overhang
Goodheart-Willcox Publisher

## Slide 31: Framing Under Slate or Tile
Requires substantial base
Concrete base needs lowered floor framing
Smaller size joists reduce space between joists
Beams under section used to support added weight
Cement mortar mix used

## Slide 32: Engineered Wood Products (EWPs)
Combine wood veneers, fibers with adhesives to form beams, headers, joists, and panels
Advantages: High quality and consistency; no knots, checks, warps; 8% to 12% moisture content; design flexibility
Disadvantage: Lack of industry standards

## Slide 33: Oriented Strand Board (OSB)
Made from long strands of wood and resin
Aspen is preferred wood
Advantages:
  Less expensive than plywood
  Unique appearance
Disadvantages:
  Subject to swelling
  Not designed for exposure to elements

## Slide 34: Oriented Strand Board (OSB)
Made in panel sizes, typically 4' x 8'
Available in sizes up to 8' x 24'
1/8" space along edges prevents buckling
Use same nailing schedules used on plywood

## Slide 35: Parallel Strand Lumber (PSL)
Made from thin strands of wood
Used for beams, columns, headers
High strength and span capacity
Low moisture content eliminates shrinking and checking
Large billets, 11" x 17", formed and then sawed to specific sizes

## Slide 36: Parallel Strand Lumber (PSL)
Advantages:
  Strong
  Longer spans create more design flexibility
Disadvantages:
  Engineered connections required for side-loading multiple-ply beam
  Should not be drilled or notched
  Must be stored on site to prevent swelling

## Slide 37: Parallel Strand Lumber (PSL)
Widths from 1-3/4" to 7"
Two plies of 2-11/16" members match typical 5-1/2" wall
Lengths up to 66'
Eliminates need for built-up beams
Alpine Structures

## Slide 38: Laminated Veneer Lumber (LVL)
Veneers stacked parallel to each other
Used for headers, beams, joists, columns, and flanges for wood I-beams
All plies parallel to provide maximum strength
Woods of choice are southern yellow pine and Douglas fir

## Slide 39: Laminated Veneer Lumber (LVL)
Advantages:
  High strength allows long spans
  Can be built-up on site to form larger members
Disadvantages:
  More expensive than solid lumber
  Lower moisture content than solid lumber
  Must be sized for specific load conditions

## Slide 40: Laminated Veneer Lumber (LVL)
1-3/4" billet most common
Use individually for joists or combined to form headers or beams
Depths from 5-1/2" to 18", lengths up to 66'
Should not be mixed with solid lumber in same floor assembly
Beams should not be drilled

## Slide 41: Glue-Laminated Lumber
Also called glulam beams
1x or 2x lumber glued in stacks to desired shape and size
  Virtually any length or depth can be produced
Manufactured to national standard
Grades available: Framing, industrial, architectural, premium

## Slide 42: Glue-Laminated Lumber
The Engineered Wood Association

## Slide 43: Glue-Laminated Lumber
Advantages:
  High strength
  Available either straight or cambered
  Dimensionally stable and attractive
Disadvantages:
  Expensive
  Requires special handling and storage
  Requires special equipment to handle

## Slide 44: Installation of Glue-Laminated Lumber
Technical support generally required
Manufacturers provide span charts, installation details, technical assistance
Special connectors required

## Slide 45: Wood I-Joists
2 x 4 machined-stressed lumber or LVL
Webs usually made from 3/8" OSB
Variety of flange widths, depths, lengths
Boise Cascade Corporation

## Slide 46: Wood I-Joists
Advantages:
  Speed of construction
  Knockout holes for plumbing and electrical cable
  Dimensionally stable and straight
Disadvantages:
  Require more effort to cut
  Not universally accepted

## Slide 47: Wood I-Joists
Installation similar to traditional floor joists or rafters
Should not be mixed with solid lumber in same assembly
Web stiffeners or blocks normally used at bearing points

## Slide 48: Post and Beam Construction
Posts, beams, and planks as framing members
Spaced farther apart than conventional framing members
Posts carry most weight
Curtain walls allow for wide glass, no headers
Foundation is continuous wall or series of piers on which each post is located

## Slide 49: Post and Beam Construction
Check local codes for post size requirements
Beam types include solid, laminated, steel-reinforced, plywood box
Spacing and span determined by size and type of materials and load to be supported
Beam placement systems include longitudinal method and transverse method

## Slide 50: Post and Beam Construction
Metal fasteners used to connect large beam segments
Goodheart-Willcox Publisher

## Slide 51: Respecting Diversity
Characteristics that vary from person to person is known as diversity
Being able to work with a diverse group is an important job skill
Getting to know those who differ from us makes us less likely to subject others to generalizations or preconceived biases we may have
Employability