## Slide 2
Chapter 25
Fireplace, Chimney, and Stove Details

## Slide 3: Objectives
Identify the parts of a standard masonry fireplace and chimney.
Compare various types of fireplaces that are appropriate for a residence.
Apply the appropriate principles to design a typical fireplace.
Explain the difference between a radiant and circulating stove.

## Slide 4: Introduction
Fireplace is an important design consideration, often a focal point
Many fireplaces fail to operate properly
Fireplaces must perform safely and according to local building codes

## Slide 5: Fireplace
Breadmaker/Shutterstock.com

## Slide 6: Parts of a Fireplace
Fire chamber
Hearth
Damper
Smoke shelf
Flue
Goodheart-Willcox Publisher

## Slide 7: Fire Chamber
Fire chamber is heart of fireplace
Lined with firebrick
Fireclay is bonding material between firebricks
Shape of fire chamber is critical
  Wall thickness on back and sides should be at least 8" thick

## Slide 8: Ash Dump
Cavity where ashes collect and be removed
Ashes are removed through cleanout
Nejron Photo/Shutterstock.com

## Slide 9: Hearth
Area around wood-burning fireplace that protects floor from sparks
Made of noncombustible material
May be even with floor or raised
Should extend at least 16" in front of fireplace
Inner hearth makes up floor of firebox

## Slide 10: Hearth
Black slate tile of this hearth extends into room to protect wood floor from sparks
Iriana Shiyan/Shutterstock.com

## Slide 11: Damper
Regulates airflow and stops downdrafts when fireplace is not operating
Located in throat of fireplace
Damper opening
  Larger than area of flue lining and as long as width dimension of fireplace
  Placed 8" above top of fireplace opening

## Slide 12: Damper
Typical design specifications
Donley Brothers Company

## Slide 13: Smoke Shelf and Smoke Chamber
Smoke shelf
  Deflects cold air flowing down chimney upward into rising warm air from fire
Smoke chamber
  Directs smoke up and away from firebox and into flue

## Slide 14: Chimney and Flue
Chimney is freestanding, vertical structure that allows smoke to leave the home
Flue is path that conducts smoke safely to top of chimney and into outside air

## Slide 15: Chimney and Flue
Recommended chimney heights above the roof
Goodheart-Willcox Publisher

## Slide 16: Flue
Begins at top of smoke chamber and extends to top of chimney
  Clay lining
  Requires at least 4" of masonry on all sides
Each fireplace must have its own flue

## Slide 17: Flue Size
At least 1/10th of fireplace opening
Proper flue size is related to fireplace opening size, flue height, flue location in structure
Flue must be at least 2' above highest point of roof

## Slide 18: Framing
Required clearances:
  2" between chimney and framing at front and sides of fireplace
  4" at back side of fireplace
Openings in floor, ceiling, and roof through which chimney passes must have double headers and trimmers

## Slide 19: Framing
Goodheart-Willcox Publisher

## Slide 20: Framing
Saddle or cricket is built on high side of chimney to shed water on single slope roof section
Goodheart-Willcox Publisher

## Slide 21: Framing
Masonry above fireplace opening on interior of house must be supported by lintel
Angle steel lintel is most common
Lintel size depends on width of fireplace opening

## Slide 22: Fireplace Design
Design factors:
  Homeowner’s preference and budget
  General style of house
Some CADD packages automate the process of specifying fireplaces

## Slide 23: Fireplace Specifications
Single-face fireplace
Two-face opposite fireplace
Two-face adjacent fireplace
Three-face fireplace

## Slide 24: Fireplace Specifications
Goodheart-Willcox Publisher

## Slide 25: Prefabricated Metal Fireplaces
Made of steel
Include:
  Inner hearth
  Fire chamber
  Throat
  Damper
  Smoke shelf
  Smoke chamber
Goodheart-Willcox Publisher

## Slide 26: Prefabricated Metal Fireplaces
Heat recirculation feature draws air in from room, heats it, and returns warmed air to room
Consult local building codes prior to installation
Heatilater, Inc.

## Slide 27: Stoves
Radiant stoves
  Warms through radiant heat, which passes through air with no assistance from airflow
Circulating stove
  Uses airflow and radiant heat
  Outer jacket facilitates air movement
  Safer and may be placed closer to combustible material than radiant stoves

## Slide 28: Catalytic Stove
Wood-burning stoves that use a ceramic catalyst for increased efficiency
Vermont Castings

## Slide 29: Stove Efficiency
Low-efficiency stoves
  20% to 30% efficient
Medium-efficiency stoves
  35% to 50% efficient
High-efficiency stoves
  Over 50% efficient

## Slide 30: Pellet Stoves
Burn pellets made from wood by-products, corn, or some types of grain
Pellets are carbon-neutral fuel and leave very little residue
Sealed, double-walled vent system is required to channel exhaust gases out
Green Architecture

## Slide 31: E-mail Etiquette
Use appropriate tone
Do not use emoticons
Mention attachments
Do not forward jokes or spam
Never use profanity or respond in anger
Avoid overuse of e-mail
Avoid using all caps
Employability